ECE591D - Embedded System Design

# Lab Phase 2

Sudhagar Thirumoolan, Vasanth Asokan, Rajkumar Nagarajan

### Various modules of our lab phase and their working are discussed below:-

- Joystick calibration: -

Joystick calibration is done at the initial state upon pressing the PD1 button. The joystick is positioned at the various extreme positions upon the toggling of LED7. And then the linearization ratios are calculated.

- SONAR Calibration: -

Sonar Calibration is done at the initial state when PD2 button is pressed. The transmitter is focused on an obstacle free direction. The truck is driven in that direction to calculate the dynamic threshold value.

- Ultrasonic Pulse Transmission: -

The pulse transmissions are initiated only on entering the automatic drive mode. And the transmit pulses are initiated using Timer0. This is achieved by using a 12.5 us period counter set using Timer0. The interrupt handler sends 5 pulses and then disables the Timer0 Counter Overflow Interrupt. Whenever the transmit function is called the Timer0 Counter Overflow Interrupt is enabled again. Whenever a pulse is sent PC0, PC1 & PC2 are toggled. The command pulse for transmission is sent through PORT E pin 6.

- Ultrasonic Pulse Reception: -

Once the transmission pulses are sent. The program keeps listening at the left & right ultrasonic receivers by doing ADC conversions fast enough for up to 8ms. These converted values are stored into an array at the ADC conversion complete handler along with their time of arrival. The time of flight is calculated using Timer1 and counting ticks as multiple of 250ns.

On receiving a valid pulse above the threshold value, on the left receiver a pulse is sent on PC1 and on the right receiver a pulse is sent on PC2.

- Distance & Azimuth Calculation: -

From the stored array of time of flight and ADC converted values, the maximum ADC values for left & right ultrasonic receivers are found out and the corresponding time of flights are used to calculate Dleft & Dright.

The formulae are given by

Dleft = Tleftecho * 250ns * 1100 ft/s;

Dright = Trightecho * 250ns * 1100 ft/s;

From these the latency difference (Trightecho – Tleftecho) is calculated and is used for Looking UP a Table of angles for the azimuth.

The distance calculation is done as given at the assignment using the formula provided.

- Manual Drive Control: -

The manual drive control is initiated by pressing PD4 at the initial state. Here the joystick is sampled regularly and then the drive control is called for the corresponding values of the sampled joystick values.

- Collision Avoidance: -

The automated collision avoidance is initiated by pressing PD0 at the initial state. The main loop keeps transmitting ultrasonic pulses then it receives signals form the receivers for about 8 ms. And after that it processes the stored data and performs distance and angle calculations. If there is a positive distance calculated in 3 consecutive loops then the automated collision avoidance routines are invoked.

Based on the angle, a decision as to whether to swerve left or right is made. A standard detour procedure is followed. Before the detour, the truck speed is brought down forcibly to a manageable level. No odometer reading is made and since the truck detour is hard-coded, the truck returns to the approximately original heading after the detour. The Obstacle distance info was not used, except to filter out distant objects.

- Drive Control:

The Drive control function can be subdivided into two independent sub-modules. The Steering Control and Motor control. Wired Input from the joystick is read through the ADC's channel 2 and 3.The ADC is run with a CK/32 clock, which provides sufficient accuracy. The raw value is passed through a piecewise linearization function, which returns linearized

X and Y values. X controls the steering and Y controls the motor input. The Truck control software detects if the joystick is unplugged, if it gives zero X and Y values. The Truck motion is stopped and the Steering is centered.

- Steering Control:

Steering Control is essentially the application of 2 signals suitably. The signal SteerL steers the wheels left and the SteerR signal steers the wheels right. The wheels might need a pulse in the opposite direction for them to reach the center position.

It takes approximately .5s from start of applying a pulse for the wheels to reach full position. Steering sensitivity was not a criterion and the steering was implemented with a big dead zone in the centre.

- Proportional Steering Control:

Essentially applying a pulse of Steer followed by a pulse of Steer simulates proportional joystick control in an otherwise un-proportional steering servo. The width of the pulse of Steer determines to what degree the direction change is achieved. So essentially it’s a software implementation of PWM to provide proportional steering control.

- Motor Control:

DriveSpeed controls the motor working. Experiments revealed that the motor turns on at around 85% duty cycle on fresh batteries, and

around 90-95% on an old set of batteries.

truck_fwd (target) - drives the truck forward with the speed. The target speed is reached by smoothly ramping up from the initial speed with which the truck moves.

truck_rev( target ) - drives the truck in reverse with the speed .

DriveDir is the signal which controls the motor direction.

- Proportional Driving Control:

Implementing a Hardware PWM signal using Timer/Counter 0 and driving the DriveSpeed signal helps control the motor. Setting OCR0 controls the duty cycle of the PWM signal. Based on JoyY info, setting the duty cycle proportionally, gives proportional steering control.

Look at Figure 2 for more details..

## Execution Time Analysis of the Program:-

Interrupt handlers involved: -

- Timer 0 interrupt – for transmission pulse generation

- ADC interrupt – for ADC conversion

Execution Time of Timer0 Interrupt:-

Timer0 executes only 10 times per main execution loop. After that it is disabled. And enabled manually in the next main loop. The interrupt takes a maximum of about

15-20 assembly instructions.

Our former implementation used Timer0 interrupts through out the main loop to measure the distance also. This increased the time period of the operation of the transmitter from 12.5uS to about 20uS. So the implementation was modified to use a non interrupt implementation . and the interrupt was used only for the pulse generation and then the interrupt  is disabled.

ADC Interrupt:-

The ADC routines are blocked until the values are returned. The duration for the conversion depends on the frequency of the operation. For the Ultrasonic receivers, the ADC is operated at a scaling factor of 2 and for the joystick it is operated at a scaling factor of 32.

The other operations of the interrupt take up utmost about 25-30 assembly instructions.

Main loop execution time:-

- initiate the transmission of pulses  				--- 	1250 us

- listening to the received echoes and storing the values	---	8000 us

- overriding joystick & executing collision avoidance		---  1880000 us

- other calculations involved is proportional to the number	---    450000 us

of echoes read in the 8ms wait time(approx. 45)

5)   Manual Joystick Drive Control				---      30000 us

does 2 ADC conversions and other control  approx

Angle calculations are done with LUTs  and distance calculations are calculated once in the main loop only if there is exceeding of the threshold value at least 3 times. Thereby minimizing the distance calculation timing. If the threshold value is not exceeded 3 times, it is assumed that there is no obstacle and control is given to the joystick drive control.

# Text boxes

Fig 2. Envelope of the Raw Signal reception at the Receiver calculated at one instance

Fig.1 Graph of the amplified signal reception at the left received

for an object at 1ft, 2ft & 3ft